## Slide 1: Basics of Electronics Engineering Topic- Rectifiers

## Slide 2: Introduction
A rectifier is a circuit which converts the alternating current (AC) input power into Direct current (DC) output power.
Diode and SCR are commonly used in rectifiers circuit.

## Slide 3: Difference between AC and DC signals
AC (ALTERNATING CURRENT) | DC (DIRECT CURRENT)
AC signal flows one way, then other way continually reverses the direction. | Direct current always flows in same direction, but it may increase or decrease.
Continually changing between positive (+) and negative (-). | A DC signal is always positive (or always negative), but it may increase and decrease.
Rate of changing direction is called frequency of the AC and measured in Hertz (Hz). | Frequency is zero.

## Slide 4: Rectification process

## Slide 5: Types of Rectifiers
Half wave Rectifier
Centre tapped Rectifier
Bridge Rectifier

## Slide 6: Half wave rectifier
In half wave rectification, either the positive or negative half of the AC wave is passed, while the other half is blocked.
Because only one half of the input waveform reaches the output, it is very inefficient if used for power transfer.

## Slide 7: Half wave rectifier working animation

## Slide 8: Half wave rectification

## Slide 9: Peak Inverse Voltage
Peak Inverse Voltage (PIV) is the maximum voltage that the diode can withstand during reverse bias condition. If a voltage is applied more than the PIV, the diode will be destroyed.

## Slide 10: Half Wave Rectifier Calculations

## Slide 11: Half Wave Rectifier Calculations

## Slide 12: Efficiency of Half wave Rectifier

## Slide 13: Efficiency of Half wave Rectifier contd.

## Slide 14: Half Wave Rectifier Calculations

## Slide 15: Centre Tapped Full wave rectifier
For single-phase AC, if the transformer is center-tapped, then two diodes back-to-back (i.e. anodes-to-anode or cathode-to-cathode) can form a full-wave rectifier.

## Slide 16: Centre Tapped Full wave rectifier

## Slide 17: Centre Tapped Full wave rectifier

## Slide 18: PIV of Centre Tapped Rectifier

## Slide 19: PIV of Centre Tapped Rectifier

## Slide 20
A bridge rectifier is an alternating current (AC) to direct current (DC) convertor.
It rectifies mains AC input to DC output.
Bridge rectifiers are widely used in power supplies.
It requires four diodes instead of two, but avoids the need for a centre-tapped transformer.
Bridge Rectifier

## Slide 21
It consist of four diodes D1, D2, D3, D4 and step down transformer with load connected resistance.
The AC voltage is first applied to primary of the transformer which is step down with the step down transformer and applied to the secondary of the transformer.
Bridge rectifier
Bridge Rectifier

## Slide 22
During positive half cycle of applied voltage:
Point A becomes at positive potential (+) whereas point B will be at negative potential (-). So diode D1 and D3 becomes forward bias and behave like a closed switch whereas diode D2 and D4 becomes in reverse bias and behaves like an open switch.
Equivalent circuit of bridge rectifier during positive half cycle
Bridge Rectifier

## Slide 23
So current will start to flow from point A through diode D1 to the point B through load resistance RL to point b through diode D3 and finally reaches to point B.
In this way the direction of current through load resistance RL is from small a to small b.
Shows the current direction through load resistance RL: A-D1-a-RL-b-D3-B
Bridge Rectifier

## Slide 24
During negative half cycle:
Point A will be at negative potential (-) whereas point B will be at positive potential.
So diode D1 and D3 comes in reverse bias and behaves like an open switch whereas diode D2 and D4 comes in forward bias and behaves like closed switch.
Equivalent circuit of bridge rectifier during negative half cycle
Bridge Rectifier

## Slide 25
So during negative half cycle, current will start to flow from point B through diode D2 to the point a through load resistance RL to point b to diode D4 and finally reaches to point A.
In this way the direction of current through load resistance RL is from small a to small b
Fig Shows the current direction through load resistance RL: B-D2-a-RL-b-D4-A
Bridge Rectifier

## Slide 26
In this way, Bridge rectifier convert both cycles of an AC voltage into DC.
AC input
D1, D3 current
D2, D4 current
Total output current
Bridge Rectifier Waveforms

## Slide 27: PIV Bridge Rectifier

## Slide 28
PIV (Peak inverse Voltage): At any instant when the transformer secondary voltage attains positive peak value Vmax, diodes D1 and D3 will be forward biased (conducting) and the diodes D2 and D4 will be reverse biased (non conducting). If we consider ideal diodes in bridge, the forward biased diodes D1 and D3 will have zero resistance. This means voltage drop across the conducting diodes will be zero. This will result in the entire transformer secondary voltage being developed across load resistance RL.
Thus PIV of a bridge rectifier = Vmax (max of secondary voltage)
PIV Bridge Rectifier

## Slide 29: Full Wave Rectifier Calculations: 1. DC Voltage

## Slide 30: Full Wave Rectifier Calculations:

## Slide 31: Full Wave Rectifier Calculations:

## Slide 32: Full Wave Rectifier Calculations:

## Slide 33: Comparison of different Rectifiers

## Slide 34: Numericals

## Slide 35: Numericals

## Slide 36: Numericals

## Slide 37: Numericals